Crib sheet

| Fuel | Heating value (energy content) – Ei | Unit | Price – Pi | Unit | Thermal Efficiency - ( | Unit | Fuel cost | Unit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Coal | 24.9 | GJ/ton | 0.058 | £/ton |  | n.a. |  | £/MWh |
| Gas | 0.0357 | GJ/m3 | 29.468 | £/m3 |  | n.a. |  | £/MWh |
| Uranium | 3900 | GJ/kg | 637.58 | £/kg |  | n.a. |  | £/MWh |

Fuel i cost = 1/( * 1/[Ei/3.6] * Pi

Notes:

1 MWh = 3.6 x 109 Joules (J) = 3.6 GJ = 3600 MJ

Both Wh and Joule are units of energy, i.e. the energy transferred to (or work done on) an object when a force of one newton acts on that object in the direction of its motion through a distance of one meter.

Watt (W) is the unit of power, i.e. one Joule of energy being uniformly transferred over a period of one second (s). That is, W = J/s.

Thermal efficiency ratio:  ( ( energy output (J) / energy input (J). The higher the ratio, the more electric energy is extracted from one unit of energy contained in the fuel.

Producing 1 MWh (= 3.6 GJ) of electric energy requires 1/( MWh of (input) energy.

- Demand curves – Round 0

Off-peak hours	Volume =  –5 * price + 21,840

Shoulder hours	Volume =  –5 * price + 38,245

Peak hours		Volume =  –5 * price + 59,880

- Number of hours

Off-peak	5000

Shoulder	3600

Peak		160

(Total 	8760 = 24 hours * 365 days)

- Carbon conversion factors

Coal-fired 		0.330	tonnes of CO2 per 1 MWh of fuel

CCGT, Gas-fired	0.185	tonnes of CO2 per 1 MWh of fuel